## Slide 1: Animal Trap Camera
Andy Lepetri

## Slide 2: What is it?
Used for
  Research
  Recreational
Deliverables
  Photos
  Videos
  Time logs
http://www.trailcamproblog.com/page/51/
http://www.trailcamproblog.com/page/51/

## Slide 3: Why do so?
My Wife
Open Source
  Machine Learning Animal Identification
Price
  ~$60 vs >$400
Contribution to Research
  iNaturalist
https://www.inaturalist.org/pages/getting+started
https://www.idigbio.org/content/inaturalist-workshop-report

## Slide 4: How? Original Plan
Raspberry Pi 2 B+
  Python 3.5
  OpenCV
Pi NoIR Camera
  No IR Filter
OSEPP PIR Sensor
  Motion
IR Illuminator
Flash Drive
  Automatic External Storage
https://www.lifewire.com/best-usb-flash-drives-4141193
https://www.amazon.com/Raspberry-Pi-Model-Desktop-Linux/dp/B00T2U7R7I
https://www.raspberrypi.org/products/pi-noir-camera-v2/
https://www.osepp.com
https://www.amazon.com/gp/product/B075ZYG89D/ref=oh_aui_detailpage_o05_s00?ie=UTF8&psc=1

## Slide 5: How? Successful Additions
Power Relay
  5V Coil for Pi GPIO Control
General Purpose Battery
  12V DC
Power Converter
  12V DC to 5V DC
https://www.amazon.com/gp/product/B00E0NTPP4/ref=oh_aui_detailpage_o00_s00?ie=UTF8&psc=1
https://www.amazon.com/gp/product/B00CXKBJI2/ref=oh_aui_detailpage_o00_s00?ie=UTF8&psc=1
https://batteryspecialists.com.au/fusion-12v-5-4ah-general-purpose-agm-battery.html

## Slide 6: Design Change

## Slide 7: Testing
NoIR Pi Cam
PIR Sensor
12V Battery
Raspberry Pi 2+
IR Illuminator
Power Converter
Indicator LED
Interface Button
5V Relay

## Slide 8: Testing: Functionality
Complete darkness
Extended periods of time between test subjects
Varying speeds of subjects
Confirmation that illuminator turns off between motion capture

## Slide 9: Testing: Code Breakdown
Functionality:
  Automatically boots into script upon receiving power using the Pi’s crontab
  Waits for confirmation of mounted flash drive, then indicates ready
  Creates unique folder in flash drive and labels images uniquely
  Button hold of 4 seconds triggers start main program loop
  Main loop continues until photo limit is reached, or button is held
  Categorizes photos into groups of motion
  Shuts down automatically at the end of script
  Safe flash drive removal

## Slide 10: Struggles
Software:
  Being able to recognize a mounted folder
  Turning off the Pi Cam properly while troubleshooting
  Setting up a consistent remote desktop, automatically connecting to multiple wifi’s
Mechanical:
  Many, many redesigns
  Two days of constant 3D printing
  Hinges were too weak
  Form factor
Electrical:
  The wiring is a mess… but functional

## Slide 11: Appendix
IR Illuminator
  90° Field of View
  Illuminates up to 80 ft
Pi NoIR Camera
  62° x 49° FOV
  Fish-eyed lens can be added
OSEPP PIR Sensor
  120° FOV
  Minimum 4 seconds between new motion
https://www.amazon.com/gp/product/B075ZYG89D/ref=oh_aui_detailpage_o05_s00?ie=UTF8&psc=1